## Slide 1
Schedule-Free Autonomous Passenger Boats in Bergen
From navigable routes and synthetic demand to heuristics and reinforcement learning
Master's project — NHH Norwegian School of Economics
Haider Yesid Fonseca Najar
Bergen, 2026
SAY: The project asks how a schedule-free water-taxi service can dispatch a fleet in real time when demand is stochastic.

## Slide 2
Presentation roadmap
02
NHH — Schedule-Free Autonomous Passenger Boats in Bergen
SAY: Problem → data → heuristics → fleet sensitivity → reward design → PPO → final comparison.
• Problem and motivation
• Network and navigable routes
• Demand generation and assumptions
• Simulation and metrics
• H0 → H1 → H2 → H3 heuristics
• Fleet-size sensitivity
• Reward experiments
• PPO formulation and final training
• H0 / H3 / PPO comparison
• Conclusions and limitations

## Slide 3
1. Problem: a schedule-free water taxi
03
NHH — Schedule-Free Autonomous Passenger Boats in Bergen
SAY: This is a dynamic dispatch problem, not a fixed timetable problem.
• Passengers arrive dynamically at multiple waterfront nodes.
• There is no fixed timetable: boats decide where to go every decision epoch.
• A free boat can serve local demand, reposition toward remote demand, or wait.
• The fleet must reduce passenger waiting while avoiding unnecessary empty movements.
• Research question: how should a stochastic fleet be dispatched using only currently observable demand?
Core decision
For every free boat: where should it go now — or should it wait?

## Slide 4
2. Research context
04
NHH — Schedule-Free Autonomous Passenger Boats in Bergen
SAY: The Bergen literature motivates autonomous ferries; this project focuses on the real-time dispatch layer.
• Braathen, Góez & Guajardo (2024) study autonomous versus crewed ferry operations in Bergen.
• Their models construct passenger transportation plans and identify potential benefits of autonomy, especially in low-demand hours.
• This project instead studies schedule-free, real-time fleet dispatch under stochastic arrivals.
• The contribution is a common simulation environment for transparent heuristics and PPO.
Braathen, C., Góez, J. C., & Guajardo, M. (2024). Maritime Transport Research, 7, 100115. DOI: 10.1016/j.martra.2024.100115

## Slide 5
3. System architecture
05
NHH — Schedule-Free Autonomous Passenger Boats in Bergen
SAY: Geography defines the routes, demand generates requests, the simulator exposes the state, and the policy decides.
1. Geography
4 demand nodes Water-based routes
2. Demand
OD intensity Time-varying arrivals
3. Simulator
2-min steps Queues + boats
4. Policy
H0–H3 PPO
Same simulator • same demand • same metrics

## Slide 6
4. Navigable network

## Slide 7
4. Navigable network
Four demand nodes → six pairwise routes
06
NHH — Schedule-Free Autonomous Passenger Boats in Bergen
SAY: Before dispatching anything, we need realistic routes and travel times that do not cross land.
Navigable route map
INSERT FIGURE / MEDIA bergen-boats/02_ruteo_navegable/output/mapa_rutas_navegables.png
• Bryggen, Kleppestø, Laksevåg and Sandviken.
• Six pairwise connections.
• Dijkstra over a water-classified map.
• Travel-time matrix is fixed and reused by all modules.
• Final configuration uses 30 km/h effective speed.

## Slide 8
5. Route assumptions and validation
07
NHH — Schedule-Free Autonomous Passenger Boats in Bergen
Element | Final choice
Network | 4 demand nodes; 6 pairwise connections
Route calculation | Shortest navigable path over water; Dijkstra
Speed | 30 km/h
Decision interval | Every 2 minutes
Travel | Direct origin → destination; no multi-stop
Capacity | 30 passengers in final PPO scenario
Transit | Boats cannot be redirected mid-route

## Slide 9
6. Demand generation
Synthetic demand anchored in open data
08
NHH — Schedule-Free Autonomous Passenger Boats in Bergen
SAY: The service does not exist, so there is no observed ridership. The model therefore constructs realistic demand patterns from spatial information.
• Population/spatial information is used to construct OD demand intensity.
• A gravity-style formulation combines origin mass, destination attractiveness and distance decay.
• Time-of-day roles create different directional patterns.
• Arrivals are stochastic; training can therefore see fresh demand realizations.
• The final fleet/PPO scenario uses a 10% demand scale.
Demand / OD figure
INSERT FIGURE / MEDIA demand/output/ or demand/notebooks/02_patron_od.ipynb
flow(i,j) = mass_origin(i) x mass_dest(j) x exp( - time(i,j) / tau )

## Slide 10
7. Demand intensity as an experimental parameter
09
NHH — Schedule-Free Autonomous Passenger Boats in Bergen
SAY: The demand scale is a controlled stress parameter, not a claim about future ridership.
• Low demand emphasizes idle capacity and unnecessary repositioning.
• Higher demand increases queue pressure and waiting time.
• Fleet-size experiments therefore reveal how much capacity is needed for a given demand level.
• The final comparison fixes demand at 10% so H0, H3 and PPO face exactly the same workload.
Demand sensitivity plot
INSERT FIGURE / MEDIA Insert demand-by-time / demand-level plot from demand notebooks

## Slide 11
8. Simulation loop
10
NHH — Schedule-Free Autonomous Passenger Boats in Bergen
SAY: Every policy sees the same state and cannot use demand that has not arrived.
• 1. Observe queues, boat positions and free/occupied status.
• 2. Each free boat chooses one destination or waits.
• 3. The chosen OD queue boards FIFO passengers up to capacity.
• 4. Advance the clock by 2 minutes.
• 5. Arriving boats unload; new arrivals become visible only at the next decision.
• 6. Repeat until the horizon ends.
Information constraint
No policy sees future arrivals.

## Slide 12
9. Evaluation metrics
Operational outcomes, not reward values
11
NHH — Schedule-Free Autonomous Passenger Boats in Bergen
SAY: The final comparison is based on passenger and fleet outcomes, not on the numerical reward.
Metric | Meaning
Mean wait | Typical passenger waiting time
P95 / max wait | Tail and worst-case waiting
Mean system time | Waiting + in-boat travel
% served | Completed trips before horizon end
Final backlog | Still queued or onboard at horizon end
Empty movements | Repositioning without passengers
Fleet waiting/free | Share of fleet time not serving

## Slide 13
2
Heuristic dispatch policies
Each section answers one question and builds on the previous one.
SAY: The heuristic stage builds a transparent sequence: each new policy adds one idea.

## Slide 14
10. H0 — Reference policy
Nearest-available, local-first
13
NHH — Schedule-Free Autonomous Passenger Boats in Bergen
SAY: H0 serves local demand first; if none exists, it repositions toward the most urgent remote queue.
Decision rule
1. Local demand exists → destination with oldest waiting passenger. 2. No local demand → remote queue with greatest waiting time; tie-break by travel time. 3. No demand → wait.
Why H0 matters
Transparent No calibrated weights No forecasting Strong reference policy Same simulator as every later policy

## Slide 15
11. H1 — Persistent reservations
14
NHH — Schedule-Free Autonomous Passenger Boats in Bergen
SAY: H1 keeps H0's dispatch rule but prevents multiple free boats from chasing the same remote queue.
• H1 = H0 + persistent reservation.
• A repositioning boat reserves its remote OD queue.
• The reservation remains active while the boat is committed.
• Other free boats discount reserved capacity.
• This fixes a coordination problem across decision epochs.
H1 animation
INSERT FIGURE / MEDIA heuristicas/outputs/figuras/ (H1 GIF)

## Slide 16
12. H2 — Cost within local/remote classes
15
NHH — Schedule-Free Autonomous Passenger Boats in Bergen
SAY: H2 adds a cost function but preserves strict local-first behavior.
C(b,q) = T_pickup(b,q) − W_max(q)
• T_pickup = time for boat b to reach queue origin.
• W_max = waiting time of oldest passenger.
• Local demand → compare only local queues.
• No local demand → compare only remote queues.
• For local queues T_pickup = 0, so H2 reproduces H0 locally.
• The cost mainly changes which remote queue is selected.
H2 animation
INSERT FIGURE / MEDIA heuristicas/outputs/figuras/ (H2 GIF)

## Slide 17
13. H3 — Global cost
The key heuristic
16
NHH — Schedule-Free Autonomous Passenger Boats in Bergen
SAY: H3 removes the local-first partition: every queue competes globally using the same cost.
C(b,q) = T_pickup(b,q) − W_max(q)
• Local and remote queues compete simultaneously.
• Choose the minimum-cost queue.
• A remote queue can beat a local queue only when its waiting-time advantage is large enough.
• Threshold: W_remote > T_pickup + W_local.
• This explicitly trades urgency against repositioning time.
H3 animation
INSERT FIGURE / MEDIA heuristicas/outputs/figuras/ (H3 GIF)

## Slide 18
14. Controlled tests before fleet experiments
17
NHH — Schedule-Free Autonomous Passenger Boats in Bergen
SAY: Small constructed cases verify the logic before using aggregate performance results.
Test | Purpose | Result
Two boats, same remote queue | Avoid duplicate repositioning | H1–H3 coordinate; H0 exposes known baseline issue
Reservation + new arrivals | Persistence | Reservation remains active
Demand > capacity | Boarding | FIFO up to capacity; queue remains
Local vs remote urgency | Cost threshold | H2 stays local; H3 crosses threshold
No demand | Idle rule | Policies wait

## Slide 19
15. Heuristics: fleet-size sensitivity
5 seeds × fleet sizes 4–16
18
NHH — Schedule-Free Autonomous Passenger Boats in Bergen
SAY: H3's advantage becomes visible when we vary fleet size under identical demand and simulation conditions.
Chart: 
| 4 | 6 | 8 | 10 | 12 | 14 | 16
H0 | 73.9 | 26.6 | 12 | 7.6 | 6.2 | 5.6 | 5.5
H1 | 71.5 | 25.4 | 12 | 7.8 | 7.3 | 7.1 | 7.2
H2 | 72.2 | 25.7 | 12 | 7.8 | 7 | 6.8 | 6.7
H3 | 72.9 | 24.3 | 10.6 | 6.3 | 4.8 | 4.4 | 4.1
• At 12 boats: H3 = 4.81 min mean wait.
• H0 = 6.18; H1 = 7.30; H2 = 6.95.
• H3 improves mean waiting time across the tested fleet sizes.
• Benefits of extra boats show diminishing returns.

## Slide 20
16. Heuristics at 12 boats
Full day, 10% demand, capacity 30
19
NHH — Schedule-Free Autonomous Passenger Boats in Bergen
SAY: Twelve boats is the fleet size carried into the final PPO comparison.
Metric (12 boats) | H0 | H1 | H2 | H3
Served (%) | 99.58 | 99.46 | 99.36 | 99.61
Final backlog | 34.2 | 44.0 | 52.8 | 31.8
Mean wait (min) | 6.18 | 7.30 | 6.95 | 4.81
P95 wait (min) | 15.71 | 17.71 | 17.48 | 12.27
Max wait (min) | 28.03 | 37.28 | 31.64 | 18.36
Mean travel (min) | 9.79 | 9.79 | 9.79 | 9.79
Mean system (min) | 15.97 | 17.09 | 16.74 | 14.60
Total movements | 1268.6 | 848.4 | 849.8 | 803.2
Empty movements | 704.0 | 307.8 | 303.0 | 200.6
Loaded movements | 564.6 | 540.6 | 546.8 | 602.6
Fleet occupancy (%) | 16.31 | 16.29 | 16.28 | 16.32
Fleet waiting/free (%) | 26.28 | 50.79 | 51.34 | 54.25
H3 combines lower passenger waiting with fewer empty movements than the other heuristic policies.

## Slide 21
17. What changes operationally at 12 boats?
20
NHH — Schedule-Free Autonomous Passenger Boats in Bergen
SAY: H3 is not simply moving more: it has fewer empty movements and more loaded movements.
Chart: 
| H0 | H1 | H2 | H3
Empty | 704 | 307.8 | 303 | 200.6
Loaded | 564.6 | 540.6 | 546.8 | 602.6
Chart: 
| H0 | H1 | H2 | H3
Fleet waiting/free % | 26.28 | 50.79 | 51.34 | 54.25
At 12 boats, demand does not require the whole fleet continuously; a large idle share is therefore expected.

## Slide 22
18. Heuristic visual comparison
Use animations here
21
NHH — Schedule-Free Autonomous Passenger Boats in Bergen
SAY: The animations show the actual dispatch behavior behind the averages.
H0
INSERT FIGURE / MEDIA heuristicas/outputs/figuras/h0*.gif
H1
INSERT FIGURE / MEDIA heuristicas/outputs/figuras/h1*.gif
H2
INSERT FIGURE / MEDIA heuristicas/outputs/figuras/h2*.gif
H3
INSERT FIGURE / MEDIA heuristicas/outputs/figuras/h3*.gif

## Slide 23
3
Reinforcement learning
Each section answers one question and builds on the previous one.
SAY: The heuristics establish a strong transparent baseline. PPO asks whether a learned policy can discover useful dispatch behavior.

## Slide 24
19. PPO as a sequential decision problem
22
NHH — Schedule-Free Autonomous Passenger Boats in Bergen
SAY: The simulator is formulated as an MDP: state, action, transition, reward and repeated interaction.
Component | Project definition
State | Queues, boat locations, in-transit status, onboard passengers and time
Action | One destination/wait choice per free boat
Action space | MultiDiscrete: 5 choices per boat
Transition | 2-minute step; boarding, travel, arrivals, new demand
Reward | Passenger-time penalty
Policy | PPO actor-critic trained from simulation

## Slide 25
20. How PPO works here
23
NHH — Schedule-Free Autonomous Passenger Boats in Bergen
SAY: PPO collects experience, estimates how good the decisions were, and updates the policy conservatively.
1. Observe
Queues Boat positions Time
2. Act
One action per free boat
3. Learn
Rollout Advantage Clipped update
Repeat across many stochastic demand realizations

## Slide 26
21. Reward design: what should PPO optimize?
24
NHH — Schedule-Free Autonomous Passenger Boats in Bergen
SAY: The reward is a modeling decision: it translates the operational objective into the learning signal.
• The passenger-centered objective is to reduce time spent in the system.
• Movement matters operationally, but mixing movement directly into the reward introduces a scale trade-off.
• The reward study therefore tests multiple formulations before choosing the final one.
• All reward formulations are compared using real simulator metrics, not reward magnitude.
Principle: choose the reward because of the policy it produces.

## Slide 27
22. Reward experiments: operational results
Historical reward-selection experiment
25
NHH — Schedule-Free Autonomous Passenger Boats in Bergen
SAY: D produced the strongest documented passenger-time profile among the tested formulations.
Reward | Concept | Mean system | Max system | Mean wait | Moves | Served*
B | Quadratic excess after 12 min | 29.02 | 60.77 | 17.06 | 191 | 88.0%
C | B + potential shaping | 29.25 | 74.07 | 20.21 | 193 | 84.47%
D | Pure quadratic time | 25.73 | 51.92 | 16.21 | 174 | 84.47%
E | Linear raw time | 41.06 | 123.13 | 24.41 | 172 | 74.82%
F | Quadratic raw time | 33.05 | 81.13 | 22.78 | 183 | 75.88%
G | Incremental time | 33.46 | 109.74 | 20.72 | 169 | 74.35%
H | 95/5 time + movement | 37.15 | 103.74 | 24.94 | 194 | 81.41%
*Served is contextual; selection focuses on passenger time and movements.
D: 25.73 min mean system • 51.92 min maximum system • 16.21 min mean wait • 174 movements

## Slide 28
23. Final reward choice: D
26
NHH — Schedule-Free Autonomous Passenger Boats in Bergen
SAY: D gives an increasingly strong penalty to long passenger times.
Rₜ = − Σᵢ (Tᵢ,ₜ / 12)²
• T is accumulated passenger time in the system.
• The square makes long delays disproportionately expensive.
• 12 minutes is a reference scale, not a hard service guarantee.
• No movement penalty is included in D.
• VecNormalize is used during PPO training and evaluation.
Example: 24 minutes gives 4× the squared-time penalty of 12 minutes.

## Slide 29
24. Final PPO experiment
Full-day scenario
27
NHH — Schedule-Free Autonomous Passenger Boats in Bergen
SAY: The final experiment moves from the small reward-selection instance to the full-day 12-boat scenario.
Parameter | Final value
Demand | 10%
Window | 06:00–24:00
Time step | 2 min
Episode length | 540 steps
Fleet | 12 boats
Capacity | 30
Reward | D
n_steps | 540 — one full day per rollout
Total timesteps | 1,000,000
Training seed | 123
Evaluation seeds | 1001–1005
VecNormalize | Yes

## Slide 30
25. Why 540 steps and 1,000,000 timesteps?
28
NHH — Schedule-Free Autonomous Passenger Boats in Bergen
SAY: A full day is exactly 540 two-minute steps, and the final training budget is deliberately large enough for a long-horizon problem.
• 18 hours = 1,080 minutes.
• 1,080 / 2 = 540 steps per episode.
• n_steps = 540 makes each PPO rollout one complete operating day.
• 1,000,000 timesteps correspond to about 1,852 rollouts/updates.
• This is a training-budget choice, not a claim that 1M is mathematically optimal.
Final experiment: 12 boats • 10% demand • 06:00–24:00 • capacity 30 • reward D

## Slide 31
26. PPO final results
To be filled from the 1M-timestep run
29
NHH — Schedule-Free Autonomous Passenger Boats in Bergen
SAY: Do not invent these numbers. Insert the final evaluation over seeds 1001–1005 when the training run finishes.
PPO evaluation table / plots
INSERT FIGURE / MEDIA modelo_rl/modelos/ppo_dia_10pct_12barcos_reward_D_1M/ + evaluation output
Use operational metrics: mean wait, P95 wait, max wait, system time, backlog, served %, total and empty movements.

## Slide 32
27. Final comparison: H0 vs H3 vs PPO
Same demand seeds, same simulator, same fleet
30
NHH — Schedule-Free Autonomous Passenger Boats in Bergen
SAY: This is the key scientific comparison. Interpret each metric separately.
Metric | H0 | H3 | PPO
Mean wait (min) | 6.18 | 4.81 | INSERT
P95 wait (min) | 15.71 | 12.27 | INSERT
Max wait (min) | 28.03 | 18.36 | INSERT
Mean system (min) | 15.97 | 14.60 | INSERT
Served (%) | 99.58 | 99.61 | INSERT
Final backlog | 34.2 | 31.8 | INSERT
Total movements | 1268.6 | 803.2 | INSERT
Empty movements | 704.0 | 200.6 | INSERT
Fleet waiting/free (%) | 26.28 | 54.25 | INSERT
PPO cells are intentionally left for the final 1M-timestep evaluation.

## Slide 33
28. Metric-by-metric comparison
Recommended final results slide
31
NHH — Schedule-Free Autonomous Passenger Boats in Bergen
SAY: Mean wait is typical experience; P95/max show tail risk; system time captures the full journey; empty movements show fleet cost.
Four-panel final chart
INSERT FIGURE / MEDIA Create from final evaluation CSV: wait / P95 / system time / empty movements

## Slide 34
29. Final visual comparison
H0 vs H3 vs PPO
32
NHH — Schedule-Free Autonomous Passenger Boats in Bergen
SAY: The final animations make the behavioral differences visible, not just the averages.
H0
INSERT FIGURE / MEDIA heuristicas/outputs/figuras/h0*.gif
H3
INSERT FIGURE / MEDIA heuristicas/outputs/figuras/h3*.gif
PPO
INSERT FIGURE / MEDIA PPO final GIF

## Slide 35
30. Conclusions
33
NHH — Schedule-Free Autonomous Passenger Boats in Bergen
SAY: The contribution is the complete experimental chain: network → demand → simulator → heuristics → reward design → PPO.
• A complete simulation pipeline was built for schedule-free passenger boat dispatch in Bergen.
• Navigable routes were generated from geography and reused consistently across experiments.
• Synthetic demand combines spatial and temporal assumptions with stochastic arrivals.
• H0–H3 were developed incrementally and validated through controlled cases.
• H3 is the strongest documented heuristic in the 4–16 boat fleet sweep.
• Reward design materially changes PPO behavior; D was selected from the reward experiments.
• The final PPO experiment tests whether learned dispatch can compete with transparent real-time rules.

## Slide 36
31. Limitations and what the results do NOT claim
34
NHH — Schedule-Free Autonomous Passenger Boats in Bergen
SAY: These limitations define the scope of the conclusions.
• Demand is synthetic because the service does not yet exist; it is not validated against observed ridership.
• Passengers do not abandon the system because of waiting.
• Heuristics do not forecast future demand and do not use multi-stop trips.
• The comparison is against dispatch heuristics, not a mathematical optimum.
• PPO must be tested on additional demand levels and fleet sizes before claiming broad generalization.
• The reward search is evidence-based, not exhaustive.

## Slide 37
32. Next steps
35
NHH — Schedule-Free Autonomous Passenger Boats in Bergen
SAY: The natural next step is generalization and robustness, not arbitrary tuning.
• Evaluate PPO across additional demand realizations and fleet sizes.
• Test generalization across demand intensities and time-of-day profiles.
• Investigate variable fleet sizing across the day, motivated by idle capacity at lower demand.
• If needed, introduce passenger service guarantees or patience as a separate modeling extension.
• Future work could compare against a stronger optimization benchmark.

## Slide 38
33. Key references
36
NHH — Schedule-Free Autonomous Passenger Boats in Bergen
• Braathen, C., Góez, J. C., & Guajardo, M. (2024). Autonomous ferries in light of labor regulations — A passenger perspective. Maritime Transport Research, 7, 100115.
• Schulman, J. et al. (2017). Proximal Policy Optimization Algorithms.
• Ng, A. Y., Harada, D., & Russell, S. (1999). Policy invariance under reward transformations: Theory and application to reward shaping.
• Project repository: HaiderFonseca/NHH-Schedule-Free-Autonomous-Boats-in-Bergen.

## Slide 39
Thank you
Questions
The central question is how much can be gained by moving from transparent dispatch rules to a learned real-time policy.

## Slide 40
BACKUP — Metric definitions
101
NHH — Schedule-Free Autonomous Passenger Boats in Bergen
Metric | Definition
pct_atendidas | Completed trips / generated demand
backlog_final | Still queued + onboard at horizon end
wait mean/P95/max | Completed passengers
system mean | Wait + travel for completed passengers
occupancy | Mean onboard / capacity
fleet waiting/free | Average share of boat-time free

## Slide 41
BACKUP — Heuristic comparison
102
NHH — Schedule-Free Autonomous Passenger Boats in Bergen
Policy | Reservation | Cost | Rule
H0 | No | None | Local-first
H1 | Yes | None | Local-first
H2 | Yes | T_pickup−W_max | Local-first, cost within class
H3 | Yes | T_pickup−W_max | Global cost

## Slide 42
BACKUP — Reward formulas
103
NHH — Schedule-Free Autonomous Passenger Boats in Bergen
• A: direct accumulated active-person time.
• B: quadratic excess after 12 minutes.
• C: B + potential-based shaping.
• D: pure quadratic passenger time.
• E: linear raw time.
• F: quadratic raw time.
• G: incremental time.
• H: 95/5 quadratic time + movement.

## Slide 43
BACKUP — Likely questions
104
NHH — Schedule-Free Autonomous Passenger Boats in Bergen
Question | Answer
Why synthetic demand? | The service does not exist; no observed ridership is available.
Why PPO? | MultiDiscrete action: one decision per boat.
Why no MILP? | The project focuses on real-time dispatch and learning.
Why H3? | Strongest documented heuristic in fleet sweep.
Why D? | Strongest documented passenger-time profile in reward experiment.
Why n_steps=540? | A full 06–24 day is 540 two-minute steps.
Does PPO beat H3? | Only answer after final 1M evaluation.

## Slide 44
BACKUP — Figure locations
105
NHH — Schedule-Free Autonomous Passenger Boats in Bergen
• Route map: bergen-boats/02_ruteo_navegable/output/mapa_rutas_navegables.png
• Route comparison: bergen-boats/02_ruteo_navegable/output/mapa_zoom_bryggen_comparacion.png
• Water mask: bergen-boats/02_ruteo_navegable/output/mapa_mascara_agua.png
• Travel-time heatmap: bergen-boats/02_ruteo_navegable/output/heatmap_tiempos_navegables.png
• Heuristic GIFs: heuristicas/outputs/figuras/
• Fleet plots: heuristicas/notebooks/03_comparacion_flota.ipynb
• Demand plots: demand/output/ and demand/notebooks/02_patron_od.ipynb