## Slide 1
Schedule-free autonomous boats in Bergen
Dispatch heuristics and reinforcement learning for real-time on-demand fleet operation
NHH . Supervisors: J. C. Goez, S. W. Wallace

## Slide 2
The problem
2
Bergen is fragmented by water.
Autonomous boats could link points that are close by water but far by road, with no driver and no timetable.
We study the real-time operation of such a service over four points: Kleppesto, Laksevag, Bryggen, Sandviken.
Passengers state where they want to arrive. The system decides, every 2 minutes, how the boats move.
Research question: if on-demand water transport were deployed, which operating method gives the best service. We compare a dispatch heuristic against a learned (RL) policy.

## Slide 3
Related work
3
Gu and Wallace (2021). Autonomous water taxis in Bergen. Static location, fleet and routing. DOI 10.1016/j.tre.2021.102456.
Braathen, Goez and Guajardo (2024). Autonomous ferries under labour rules. Static weekly plan. DOI 10.1016/j.martra.2024.100115.
Sanchez-Martinez et al. (2017). Schedule-free high-frequency transit. The operating idea behind this work.

## Slide 4
Contents
4
Setup: parameters and assumptions.
Step 1: navigable routing.
Step 2: demand model.
The simulator (the operating environment) and metrics.
Dispatch heuristics H0 to H3, and results.
Fleet-size sensitivity.
The reinforcement-learning model and reward design.
Results and comparison of all methods.
Conclusion.

## Slide 5
System architecture
1. Geography
4 demand nodes Water-based routes
2. Demand
OD intensity Time-varying arrivals
3. Simulator
2-min steps Queues + boats
4. Policy
H0–H3 PPO
Same simulator • same demand • same metrics

## Slide 6
Setup: parameters and assumptions
5
Item | Value / assumption
Network | 4 points, direct point-to-point trips (no multi-stop routes yet)
Time | full day 06:00 to 24:00, decisions every 2 minutes
Boat speed | 30 km/h - 16 nudos (design value)
Fleet | swept 4 to 16 boats; capacity 30 per boat
Demand | synthetic, anchored in SSB data, reference = 10% of catchment population (about 8,000 trips/day)
Passengers | They wait until served (no abandonment)
Objective | minimise passengers' time in the system

## Slide 7
Step 1. Navigable routing: method
6
Bryggen, Kleppestø, Laksevåg and Sandviken.
Straight lines between points cross land. A boat must go around the coast.
A water/land mask is built from map tiles, classifying each pixel.
Every water pixel is a graph node, linked only to water neighbours.
Water/land mask over Bergen

## Slide 8
Step 1. Result and calibration
7
Navigable routes between the four points
Dijkstra finds the shortest path that never crosses land.
Final configuration uses 30 km/h effective speed.
The output is a travel-time matrix in minutes, used by every later stage.
Travel-time matrix (minutes)

## Slide 9
Step 2. Demand model
8
No real demand exists, so it is generated, but anchored in open data.
Around each point we take the real statistical zones it serves, and read residents and jobs per zone from SSB.
Catchment zones per point (SSB)

## Slide 10
Step 2. Demand model
8
A gravity-style formulation combines origin mass, destination attractiveness.
Time-of-day roles create different directional patterns. (Morning flow toward the centre, afternoon away from it. The direction split emerges from the data, it is not imposed.)
Demand profile by hour
Arrivals follow a Poisson process whose rate rises and falls with the time band.

## Slide 11
Step 2. Demand over the day
9
Group-size distribution

## Slide 12
The simulator (the operating environment)
10
State
boat positions and occupancy, passengers waiting per origin-destination pair, time of day
Action
for each free boat, go to one of the four points, or wait
Transition
boats move on real times, demand arrives, 2-minute steps; direct trips only
Rule
queues are separate per pair; a boat serves one pair per trip, in arrival order, up to capacity
The same simulator is used by every policy (heuristic and RL), so comparisons are fair.

## Slide 13
The simulator (the operating environment)
10
State
State = {
"Boats": [
# Boat 0: Still in Bryggen, empty, no passengers
{ "Origin": "B", "Destination": "B", "min to get there": 0, "Occupation": 0 },
# Boat 1: halfway from Kleppestø to Bryggen, with 12 people, 6 min to go
{ "Origin": "K", "Destination": "B", " min to get there": 6, "Occupation": 12 }
],
"Demand waiting": {
# for each origin-destination pair: how many people and how long ago the oldest one waits
"K->B": { “persons": 15, "Wait max minute": 8 },
"K->S": { " persons ": 3, " Wait max minute ": 2 },
"L->B": { " persons ": 0, " Wait max minute ": 0 },
... (All 12 pairs)
}
"Time": { "minute": 465, “day": “lunes" }
}

## Slide 14
Evaluation metrics
10
Metric | Meaning
Mean wait | Typical passenger waiting time
P95 / max wait | Tail and worst-case waiting
Mean system time | Waiting + in-boat travel
% served | Completed trips before horizon end
Final backlog | Still queued or onboard at horizon end
Empty movements | Repositioning without passengers
Fleet waiting/free | Share of fleet time not serving

## Slide 15
Dispatch heuristics: from H0 to H3
11
H0
Local demand, send each free boat to the longest-waiting queue. Each boat decides alone.
H1
H0 + persistent reservation: once a boat commits to a queue, others do not chase it.
H2
H1 + cost function, but only within local vs remote levels.
H3
H1 + global min-cost assignment: all free boats and all queues compared together. (best)
A boat already travelling to a node, with spare capacity, may still pick up new arrivals of that same queue.

## Slide 16
H0 - Reference policy
14
NHH — Schedule-Free Autonomous Passenger Boats in Bergen
SAY: H1 keeps H0's dispatch rule but prevents multiple free boats from chasing the same remote queue.
1. Local demand exists → destination with oldest waiting passenger. 2. No local demand → remote queue with greatest waiting time; tie-break by travel time. 3. No demand → wait.
H1 animation
INSERT FIGURE / MEDIA heuristicas/outputs/figuras/ (H1 GIF)
Decision rule

## Slide 17
11. H1 — Persistent reservations
14
NHH — Schedule-Free Autonomous Passenger Boats in Bergen
SAY: H1 keeps H0's dispatch rule but prevents multiple free boats from chasing the same remote queue.
• H1 = H0 + persistent reservation.
• A repositioning boat reserves its remote OD queue.
• The reservation remains active while the boat is committed.
• Other free boats discount reserved capacity.
• This fixes a coordination problem across decision epochs.
H1 animation
INSERT FIGURE / MEDIA heuristicas/outputs/figuras/ (H1 GIF)

## Slide 18
12. H2 — Cost within local/remote classes
15
NHH — Schedule-Free Autonomous Passenger Boats in Bergen
SAY: H2 adds a cost function but preserves strict local-first behavior.
C(b,q) = T_pickup(b,q) − W_max(q)
• T_pickup = time for boat b to reach queue origin.
• W_max = waiting time of oldest passenger.
• Local demand → compare only local queues.
• No local demand → compare only remote queues.
• For local queues T_pickup = 0, so H2 reproduces H0 locally.
• The cost mainly changes which remote queue is selected.
H2 animation
INSERT FIGURE / MEDIA heuristicas/outputs/figuras/ (H2 GIF)

## Slide 19
13. H3 — Global cost
The key heuristic
16
NHH — Schedule-Free Autonomous Passenger Boats in Bergen
SAY: H3 removes the local-first partition: every queue competes globally using the same cost.
C(b,q) = T_pickup(b,q) − W_max(q)
• Local and remote queues compete simultaneously.
• Choose the minimum-cost queue.
• A remote queue can beat a local queue only when its waiting-time advantage is large enough.
• Threshold: W_remote > T_pickup + W_local.
• This explicitly trades urgency against repositioning time.
H3 animation
INSERT FIGURE / MEDIA heuristicas/outputs/figuras/ (H3 GIF)

## Slide 20
H3 cost function: minutes, no weights
12
For a boat b and a queue q (origin-destination pair):
C(b, q) = pickup_time(b, q) - longest_wait(q) + trip_time(q)
Every term is in minutes, so they are directly comparable and there are no weights to justify.
pickup_time is 0 when the boat is already at that node, so serving there becomes the cheapest option.
longest_wait enters with a minus sign: serving whoever has waited most reduces system cost.
At each step we solve a min-cost assignment of free boats to queues (greedy over the cheapest pairs).
The objective is simply to minimise minutes. Nothing arbitrary to calibrate.

## Slide 21
Heuristic results (8 boats, per component)
13
Policy | Attended % | Mean wait (min) | Mean time in system (min) | Empty moves
H0 | 99.5 | 12.0 | 21.8 | 363
H1 (+reservation) | 99.4 | 12.0 | 21.8 | 219
H2 (+local cost) | 99.3 | 12.0 | 21.8 | 223
H3 (+global cost) | 99.6 | 10.6 | 20.4 | 181
All policies serve about 99% (people wait until served), so the real differences are wait time and empty moves.
Reservation (H1) roughly halves empty moves (363 to 219). The global cost (H3) further cuts wait and empty moves.
H3 is the strongest heuristic and the benchmark for the rest.

## Slide 22
Fleet-size sensitivity (H3)
14
Chart: number of boats
| 4 | 8 | 12
H0 mean wait | 73.9 | 12 | 6.2
H3 mean wait | 72.9 | 10.6 | 4.8
4 boats saturate: waits explode (about 73 min).
8 boats already give good service.
12 boats reach about 5 min wait.
Clear diminishing returns beyond 8 to 12 boats.
This is the fleet-size vs service trade-off.

## Slide 23
Heuristics in operation
15
Live animation: H0, H1, H2, H3 side by side (plays in slideshow)
Boats move along real navigable routes.
Queues build and drain at each point.
H3 shows fewer empty repositioning moves than H0.

## Slide 24
The reinforcement-learning model
16
An agent decides, each step, where every boat goes, and learns by trial and error to maximise reward.
The action is one choice per boat (a MultiDiscrete space). DQN cannot handle this, so we use PPO.
PPO is actor-critic: a policy network chooses actions, a value network estimates how good a state is. Updates are kept small, which makes training stable.
Each training episode draws a fresh demand day, so the agent generalises instead of memorising one day.
Trained on the same scenario as the heuristics (full day, about 8,000 trips, 12 boats) for a fair comparison.

## Slide 25
Reward design (the key modelling choice)
17
The reward is the only signal the agent has. A badly designed reward is optimised in the wrong way.
We derived the base reward from the objective: penalising the people present each step equals minimising total time in system (Little's identity).
We tested several variants (see backup). The best was D:
r_t = - sum_i ( time_in_system_i / 12 )^2
The divisor 12 is only a scaling constant: scaling a reward by a positive number does not change the optimal policy, it only keeps the numbers small for stable training. 12 min is also the longest direct trip, a natural reference.
Every variant is compared on real time metrics, never on its own reward value.

## Slide 26
Results: all methods compared
18
Reward-variant study (small instance): variant D gives the best time in system.
Reward | Mean time (min) | Max time (min) | Mean wait (min)
A (linear) | 29.2 | 70.3 | 19.7
B (convex) | 29.0 | 60.8 | 17.1
C (+shaping) | 29.2 | 74.1 | 20.2
D = (T/12)² | 25.7 | 51.9 | 16.2
PASTE HERE: final comparison table RL (D) vs H0 vs H3 on the big scenario
(12 boats, full day, 10% demand) - attended %, mean/P50/P95 wait, mean/P50/P95 time in system, empty moves.
Git: run the RL notebook, then comparacion/output/tabla_comparativa.csv
Main metric is time in the system, not reward.
Expectation: the agent approaches the strong H3 heuristic and clearly beats H0.

## Slide 27
RL agent in operation
19
RL agent (seed 1001)
Baseline heuristic (seed 1001)

## Slide 28
Conclusion
20
Full pipeline built: navigable routing, data-anchored demand, a 2-minute simulator, dispatch heuristics, and a PPO agent.
The heuristic H3 (global min-cost assignment in minutes, with reservations) is strong and fully explainable: reservations cut empty moves, the global cost cuts waiting.
Fleet study shows clear diminishing returns beyond 8 to 12 boats.
The reward is derived from the objective (Little's identity), not hand-tuned; variant D gives the best time in system.
The RL agent operates the same scenario and is compared on real time metrics.
This delivers a learned, real-time, schedule-free operation, the dynamic case the earlier static models did not cover.

## Slide 29
Backup: PPO hyperparameters
BACKUP (hide before presenting)
21
Hyperparameter | Value
Algorithm | PPO (Stable-Baselines3, PyTorch)
Discount gamma | 0.99
Learning rate | 3e-4
Entropy coefficient | 0.01
Update horizon n_steps | 512
Normalisation | VecNormalize (obs and reward)
Fresh demand per episode | yes
Training steps | 1 to 2 million (until reward plateaus)
Train / eval seeds | separate (held-out evaluation)

## Slide 30
Backup: full reward-variant study
BACKUP (hide before presenting)
22
Variant | Idea | Mean time | Max time
A | linear time | 29.2 | 70.3
B | convex, tolerance, no ceiling | 29.0 | 60.8
C | B + potential shaping | 29.2 | 74.1
D | (T/12)² normalised (best) | 25.7 | 51.9
E | linear total time | 41.1 | 123.1
F | T² unnormalised | 33.0 | 81.1
G | incremental time | 33.5 | 109.7
H | other weighted | 37.1 | 103.7
All compared on real time metrics on the same held-out seeds. D wins on time in system.

## Slide 31
Backup: detail by origin-destination and boat
BACKUP (hide before presenting)
23
Compliance / service per origin-destination pair
Per-pair and per-boat metrics are available in comparacion/output for any policy.
Useful to spot which connections or boats are the bottleneck.